Works and Site Information for Civil Engineering Works

At Garrioch Drive and at the Botanic Gardens

Wards 15 and 16 Maryhill, Kelvin and Canal - October 2015

- 1.1  Introduction ; Glasgow City Council, Land and Environmental Services (the Client) intends to carry out civil engineering along the Kelvin Walkway and in the grounds of the Botanic Gardens by the spring of 2016 ; these works will be broken into two discrete pieces of work  -  each element of work will be marked and identified on drawings and detailed on a specification of works. CDM regulations will apply to this project

1.2  Work Content

  - New Entrance and Staircase at Garrioch Drive East

  - Reconstruction of collapsed walkway in Botanic Gardens

  - Directional Signage

2) Associated goals from this project;

- To demonstrate Glasgow’s commitment to the maintenance of the Kelvin Walk Way and the Botanic Gardens.

- To preserve the fabric, infrastructure and appearance of the Botanic Gardens and the Kelvin Walk Way.

- To complement ongoing restoration works in the Botanic Gardens and on the Kelvin Walkway.

- To engender a positive image of Glasgow through urban regeneration.

- To evidence the ongoing LES Parks Development Programme.

- To provide opportunities for passive recreation

- To support outdoor recreation networks for health and wellbeing.

3) This initiative complies with the intentions of the following;

- The City Council’s Strategic Plan for Health and Quality of life.

- The City Plan.

- Area Conservation Plan (DRS)

- Core Paths Strategy and National Cycling Routes

- LES Parks and Open Spaces Strategic Best Value Review.

4) Location

The precise location of the Botanic Gardens is G12, Hillhead. The nearest main roads are Great Western Road, Queen Margaret Drive, Kirklee Drive and Ford Road. The Kelvin Way meanders on the North Bank of the Botanics  towards Maryhill. The nearest main roads at this section of the walkway are Kelvin Drive, Kirklee Road, Garrioch Road and Garrioch Drive.

5) Work Content

The principal aims of this restoration is to conserve the path network in the Botanic Gardens and along the Kelvin Way for posterity and to ensure a quality parks visit for pedestrians, joggers and cyclists.   These site works require to be completed by the spring of 2016.   An element of this tender involves asphalt works, to this end the contractor is expected to remove planings / asphalt / material off site at all times and dispose of this spoilage in an appropriate manner.  The work content of the various projects can be summarised as follows;

5.1.  New Entrance and Staircase at Garrioch Drive East

The existing pedestrian entrance, staircase and approaches at the East of Garrioch Road are in extremely poor condition. The environs are overgrown and intimidating.  It is proposed that the existing pedestrian staircase is removed and replaced with a high quality replacement.  The contractor will design and install a new galvanised metal pedestrian staircase complete with handrails and painted black.  (This staircase to be of an equivalent scale and size to the existing 2.0 metre wide staircase).  This will require non slip decking and include all structural and material certification.  The contractor will also lay six new steps and tar some 13 metres of asphalt path and stairs for pedestrians  x 2.5 m wide (including aggregate and stone edging)

The contractor will then create a new 2.5 metre wide cycle entrance in the Garrioch Road  fence line , then create a 40 metres  x 2.5 wide  ‘S’ shaped asphalt path (including aggregate and stone edging). In order to build a gradual slope the contractor must allow for 30 tonnes hardcore. They will then import and lay Type 1 as fill, compacted to 200mm where required on site. This new path will provide disabled access to the Kelvin Walkway and also a safe entry point for cyclists.   Any waste generated should be transported from site and disposed of in an appropriate manner.

In order to ‘open up’ the entrances and the immediate environs, the contractor must allow for removing vegetation some 100 square metres of scrub  on both sides of the staircase being 200 m2  in total.  In conclusion, the contractor must allow for rub down, apply undercoat and two coats of black paint for 20 linear metres of gates and panels x 1.5 metres high.

5.2  Reconstruction of collapsed walkway in Botanic Gardens

There is a collapsed stretch of some ten metres of the walkway in the Botanic Gardens just behind the Kibble Palace. This collapse is 150 metres west of the Humpbacked Bridge. This breech has meant that two hundred metres of walkway had to be closed on health and safety grounds.  It is essential that a modular, galvanised metal footbridge is built as a solution to this problem and the general environs of this two hundred metre stretch of walkway re-established to ensure a safe visit for pedestrians, cyclists and runners.

The general area is heavily wooded with many large mature trees and much shrubbery. The ground surface is covered by leaf mulch. Occasional small exposures of rock can be seen on the slopes. The damaged section of walkway is on the southern bank of the R. Kelvin about 12 metres above the river bed and about 175 metres west of the footbridge leading to the Garriochmill Road. A large fallen beech tree lies below the damaged section. The slope above the damaged section is about 15 metres in height with gradients of between 1:1 and 1:2 estimated by eye. The gradient of the slope below is estimated at 1:1 or steeper. The walkway leading to the damaged section is 1.5 metres wide on both sides.

The total visual extent of the damaged section is 9.3 metres long by up to 1.5 metres wide and 2.0 metres in depth. Rock comprising sandstone is exposed immediately below the 100mm of walkway construction. It would appear that the weight of the falling tree combined with the intertwining of the roots in the discontinuities (joint, cleavage and bedding planes) of the rock strata has wrenched and broken blocks of sandstone from the solid mass. The action has resulted in short overhangs of rock and cavities in the slope. Debris comprising branches, soil and broken rock is strewn across and down the slope. Broken roots of the fallen tree can be seen lodged in the discontinuities (joints, fractures and bedding planes) of the rock.

A large rock exposure very close to the damaged section has been undercut and this has resulted in a significant overhang. A large tree sits atop this ‘promontory’ and further examination is recommended before remedial works are carried out to the damaged section of walkway.   The contractor will be responsible for all site preparation, assessment of path stability for the entire 200 metre stretch, securing approaches, rock exposures and promontory. They will remove damaged estate fencing, then design and install a modular, galvanised metal footbridge complete with handrails compliant with current regulations. The dimensions of the bridge will be 15 metres long by 2.5 metres wide. Bearings bolted an appropriate depth into the rock. The bridge will feature anti climb balustrades, including neoprene bearing pads and non-slip decking. This design will include all certification

The contractor will then clear slope above the footpath and consolidate the promontory around the bridge site, providing a retaining solution.  This new bridge and its approaches will effectively create a viewing point.

Once bridge established, the contractor will crown lift trees / cut back bushes and vegetation on both approaches to the bridge site (150 metre stretch + 50 metres stretch, being 200 metres in total).  The contractor will re-establish 2.0 metre wide path on both approaches to the bridge site (150 metre stretch  + 50  metres stretch, being 200 metres in total)  They will be expected to scrape path surface to full width and remove encroaching herbaceous vegetation. To complete the restoration the contractor will supply, spread and consolidate 50 mm layer of Raesby self-binding gravel on both approaches to the bridge site (150 metre stretch + 50 metres stretch, being 200 metres in total). Any waste generated should be transported from site and disposed of in an appropriate manner.

6) Executive Summary of Works –  In general terms  the paths and walkways  along the Kelvin Walkway and in the Botanic Gardens are in a fair condition.  As they are adjacent to the fast-flowing River Kelvin the work falls under The Water Environment (Controlled Activities) (Scotland) Regulations 2011 General Binding Rule 6 and shall be carried out to comply with this. Guidance can be found at http://www.sepa.org.uk/water/water_regulation/car_application_forms.aspx

SEPA’s Pollution Prevention Guidelines (PPG5) shall be followed, in particular section 5. They can be found at https://www.gov.uk/government/uploads/system/uploads/attachment_data/file/290145/pmho1107bnkg-e-e.pdf

(7) Expectations on Contractors

7.1  General Observations

The contractor will be expected to provide a holistic overview and consider the approaches and environs of the Botanic Gardens and the Kelvin Walkway. The successful contractor will also provide signage for the public explaining the closure of the paths/ entrances and provide a reliable time span for the restoration / closure. Vehicular entry to the site must be adequately supervised and signs directing the public provided. The Contractor shall maintain for the duration of the Contract, either on its original route or on an agreed alternative route, all Rights-of-Way and access relating to this contract.

Botanics and the Walkway are busy sites, so the contractor should be conscious at all times of the rigorous safety requirements these restorations will entail. The perimeter must be screened off with robust fencing as both sites are adjacent to the fast flowing River Kelvin and they also border an extremely busy public park. The site must be lockfast at all times and the public should not be able to gain access to the scaffolding. This consideration applies to nighttimes and at weekends. Plant should be locked down, fencing must be padlocked and ladders and tools removed from the site when the contractor leaves each night - for obvious safety requirements. Welfare facilities with a toilet and washing facilities may also be located at the site

Contractors should evidence that they are capable of producing a satisfactory method of work statement these works which will be carried out in prominent public locations. In this light the contractor should evidence that they understand the ethos of a ‘Considerate Contractor’ and are capable of responding timeously to the needs of the Client and perhaps even the Press Office of Glasgow City Council.

7.2   Requirements for the programme

Any waste generated should be transported from site and disposed of in an appropriate manner.

The Contractor will be required to submit a detailed program for approval by the Employer within 5 days of the award of the contract. The Contractor will update the program if required/if instructed by the Employer during the course of the project. Contract specific method statements and risk assessments are to be submitted for approval by the Employer prior to commencement of the Works.

The Contractor shall be deemed to have inspected and examined the sites and their environs and to have satisfied themselves before submitting their tender as to the form and nature of the sites and the extent and nature of the Works and materials necessary for providing the Works. The Contractor shall in addition be deemed to be satisfied as to the means of communication with and access to the various sites, the accommodation they may require and in general to have obtained for themselves all necessary information as to the risks, contingencies and all other circumstances influencing or affecting their tender.

The Contractor will in addition be deemed to have included in their rates for protecting the whole of the Works during the period of the Works. The Client takes no responsibility for the security of any materials, plant or tools on the varios sites and any loss or damage incurred will be bourn wholly by the Contractor.

The Contractor shall comply with any or all special requirements in relation to statutory undertakers and other bodies associated with the Works. Access to the site is restricted to the following times: No Deliveries/Uplifts or Vehicular movement outwith 08.00 and 20.00 Mon to Friday.  No works to take place Saturday, Sunday or Public Holidays-  unless by prior arrangement with the Employer.

The Contractor shall take all necessary precautions to prevent damage which may be caused by his operations to the existing surfaces, heritage gates, road pavement, drainage, outfalls, roadside drainage, kerbs, verges, road signs, park furniture, fences, etc.  In any event, the Contractor shall indemnify the Employer in respect of any consequent costs of making good any damage which may nonetheless occur as a result of his operations.

The Contractor shall not, without the prior acceptance of the Employer, carry out any operations which may affect the stability of any bridge, road, wall, gates or associated structure.  The Contractor shall carry out any instruction of the Employer to take measures which he considers necessary to protect the bridge, road or associated structure from the effects of any such operations.

Where applicable, the Contractor will be held to have identified the location of all existing live services within the vicinity of his operations and shall ensure that these are maintained at all times throughout the Contract.  Any work carried out to or which affects new or existing services must be in accordance with the Bye Laws or Regulations of the relevant Statutory Authority. The cost of repair of any damage to the existing cables and equipment shall be borne by the Contractor

No plant or materials may be stored on the site unless by prior arrangement with the Employer.  The Contractor shall make available for inspection by the Employer, copies of the written descriptions of waste and the transfer notes prepared in compliance with the Environmental Protection (Duty of Care) Regulations 1991, where applicable.

7.3   Existing Services  -   The Contractor shall ascertain from the various Public or Statutory Authorities, before works are commenced, the positions and depths of any mains, pipes, cables and other apparatus and shall take, at his expense, any and all measures reasonably required by such Authorities for the protection of their property during the progress of the work and must satisfy the Employer that the measures used are approved by the Authorities.  Any sewers or services damaged during the progress of the works shall be repaired at the Contractor’s expense and he shall report all damage immediately on occurrence.

7.4    Contractor to Protect Services  -  The Contractor shall take every precaution to avoid damage to or improper interference with the works therein referred to and he shall at his own expense, rectify any damage done and relieve the Employer of all claims in respect of any interruption or loss arising from such damage.

7.5  Contractor to Maintain Rights-of-Way    -   The Contractor shall maintain for the duration of the Contract, either on its original route or on an agreed alternative route, all Rights-of-Way and access relating to this contract.

Where a Contractor’s access crosses a right of way, adequate signing shall be erected to warn both the public and the Contractor’s operatives of the potential danger.  Where it is deemed necessary by the Employer the Contractor shall provide an operative at such a crossing to control pedestrian and vehicle movements.  All signage, fencing, etc. shall be to the satisfaction of the Contracts Administrator.

7.6  Facilities for Statutory Undertakers   -   The Contractor shall comply in every respect with the Factories Acts and the Health and Safety at Work Act 1974 and in particular with Acts concerned with safety, first aid equipment and sanitary arrangements.  Any instructions which may be given to the contractor by HM Inspector of Factories shall be complied with immediately.

7.7  Police Regulations  -   The Contractor shall ascertain the requirements for the appropriate Police Authority concerning matters which may be affected by the works.  The Contractor shall comply with any such requirements and shall allow in his Tender for any costs arising from such compliance.

7.8   Control of Construction Traffic  -  Tracked construction plant shall not run on existing carriageways or footpaths that are to be retained, nor on new carriageways or footpaths on which the wearing surface has been laid.

7.9   Roads and Footpaths to be Kept Clean  -  The Contractor shall take every precaution that may be required by the Employer to prevent dirt and mud or other material being dropped or spread by traffic from the Works on roads or footpaths in public use, or on roads being part of the Works, which are made available for use by Works traffic.  Particular attention shall be paid to the loading of lorries carrying bulk materials into the site and spoil from the site to ensure that these are not overloads, or loaded in such a way that spillage is unavoidable.  Any dirt or mud adhering to the tyres or chassis of any vehicle shall be thoroughly cleaned off by high pressure hose before the vehicle is permitted to leave the site.  In the case of delivery to the site, before the vehicle leaves the point of collection it shall be thoroughly cleaned.  The Contractor shall be equally responsible for vehicles of his sub-contractors and suppliers.

While the intention of this Clause is to prevent the spillage of dirt and mud, nevertheless the Contractor shall also be required to remove any such dirt and mud which is unavoidably split by traffic travelling to and from the site in connection with the Works, whether such  traffic is the Contractor’s or his sub-contractor’s or his supplier’s.  The roads and footpaths are to be kept in a clean condition at all times and to achieve this, especially when earth moving operations are taking place, the Contractor will require to provide suitable mechanical sweepers assisted by manual labourers.

7.10    Damage to Bridges, Walls, Gates, Roads and Property   -  The Contractor will be responsible for all repair restoration or surface damage to, or compensation in respect of paths, bridges, ornate gates and columns, public or private roads, or footpaths affected in gaining access to the site or in carrying out the work.  The Contractor shall at all times, until the expiration of the period of maintenance, keep the roads and footpaths reinstated to the satisfaction of the Authority responsible.

(8) Constraints on how the Contractor Provides the Works

8.1 	The contractor will be expected to provide clear signage at Garrioch Road and on the Kelvin Walkway – particularly if sections of the cycle way have to be closed. To reduce the risk of accidents the contractor shall erect secure Heras fencing with clear directional signage explaining the reason for closures / diversions and the expected contract duration.

8.2	The contractor must provide designed and fully certified solutions for both the reconstruction of the collapsed walkway and also for the new entrances at Garrioch Road.

8.3	Damage to Bridges, Walls, Gates, Paths, Roads and Property   -  The Contractor will be responsible for all repair restoration or surface damage to, or compensation in respect of bridges, ornate gates and columns, parks paths, public or private roads, or footpaths affected in gaining access to the site or in carrying out the work.  The Contractor shall at all times, until the expiration of the period of maintenance, keep the roads and footpaths reinstated to the satisfaction of the Authority responsible.

8.4	An element of this tender involves asphalt works, to this end the contractor shall excavate by hand and other mechanical methods (non planing) the failing asphalt surface to sound sub-base material. The contractor is expected to remove planings / spoilage / material off site and dispose of in an appropriate manner.

8.5	The contractor must confirm in writing that all works will be complete by the end of March 2016.

8.6	Contractors should evidence that they are capable of producing a satisfactory method of work statement for both the reconstruction of the collapsed walkway and also for the new staircase and the entrances at Garrioch Road. They should also confirm their awareness of weight restrictions on the paths involved.

8.7	The contractor must evidence that they employ or will engage contractors capable of working to the standards dictated by the Client.

8.8	The contractor shall evidence that it is capable of producing quality documentation at the end of the project, meticulously detailing every stage of the process, which can be kept by the Client as a detailed record of this project.

8.9	The Contractor will be required to submit a detailed program for approval by the Employer within 5 days of the award of the contract. The Contractor will update the program if required/if instructed by the Employer during the course of the project. Contract specific method statements and risk assessments are to be submitted for approval by the Employer prior to commencement of the Works.

8.10	The Contractor shall be deemed to have inspected and examined the sites and to have satisfied themselves before submitting their tender as to the form and nature of the Site and the extent and nature of the Works and materials necessary for providing the Works. The Contractor shall in addition be deemed to be satisfied as to the means of communication with and access to the various locations, the accommodation they may require and in general to have obtained for themselves all necessary information as to the risks, contingencies and all other circumstances influencing or affecting their tender.

8.11	The Contractor will in addition be deemed to have included in their rates for protecting the whole of the sites and works during the period of the Works, even when the bulk of the work is being carried out at their workshops. The Client takes no responsibility for the security of any materials, plant or tools on either site and any loss or damage incurred will be bourn wholly by the Contractor.

8.12	The Contractor shall take all necessary precautions to prevent damage which may be caused by his operations to the paths, stairs, heritage gates, road pavement, drainage, outfalls, roadside drainage, kerbs, verges, road signs, park furniture, fences, etc.  In any event, the Contractor shall indemnify the Employer in respect of any consequent costs of making good any damage which may nonetheless occur as a result of his operations.

8.13	The Contractor shall not, without the prior acceptance of the Employer, carry out any operations which may affect the stability of any path, bridge, road, wall, gates or associated structure in the Botanics or on the Walkway or their environs.  The Contractor shall carry out any instruction of the Employer to take measures considered necessary to protect the various paths and bridges, road or associated structure from the effects of any such operations.

8.14	Privacy of Information   -  The Contractor will not give any information (written or verbal) concerning the works for publication in the Press, on radio, television, internet or any other medium without the written consent of the Employer. This requirement must be included in any works or goods sub-contract.

8.15	No plant or materials may be stored on the site unless by prior arrangement with the Employer.  The Contractor shall make available for inspection by the Employer, copies of the written descriptions of waste and the transfer notes prepared in compliance with the Environmental Protection (Duty of Care) Regulations 1991, where applicable.

8.16	Scope of the Work -  A detailed Specification and Bill of Quantities is provided as part of the tender documentation.